## Slide 1: Touch Screen Smart Mirror
Kyle Skey

## Slide 2: Smart Mirror Concept
“Smart” Mirror that displays news and information
Touch screen for App selection
  (Required) One finger touch with large grid resolution (16x9)
  (Optional) One finger touch with better resolution
  (Optional) Two finger touch

## Slide 3: Design Elements/IP
IR Tx Array
IR Rx Array
Tx Controller
8-Ch ADC
I2C Serial
Signal Filtering & Integrator
Rx Controller
Computer
Display
IR Beam
I2C Protocol
IR Grid Touch Screen Grid Assembly
Intellectual Property
Circuit and PCB Design of Rx/Tx Modules
Modulation/Filtering Scheme if needed
Mechanical Packing Design
Detection Algorithm

## Slide 4: IR Grid Theory
Tx IR LEDs
Tx IR LEDs
Rx IR Phototransistors
Rx IR Phototransistors
Finger
“Dark”
“Dark”
Normal state all sensors are illuminated
Finger breaks beam in vert/horiz axis
“Dark” Rx sensors mapped to coordinate system
Rx controller sends coordinates to computer

## Slide 5: Risks and Concerns
Mechanical Alignment and Tollerances
IR Interference
Serial Protocol Issues
Funding
PCB Fab Errors
Design Errors
App Development Issues
Schedule
Full assembly Integration problems