## Slide 1
Tx
Tx Demux
Tx
Tx
Tx
Tx
Tx Demux.
Tx
Tx
Tx
Tx Serial-to-Parallel Shift Reg.
Rx
Rx
Rx
Rx
Rx
Rx
Rx
Rx
Rx Serial-to-Parallel Shift Reg
ADC0
ADC1
ADC2
ADC3
+3.3VDC
GND
Signal from Source
SW Trigger/CLK
Signal to Next Shift Reg
Sensor readings to addressable ADC
3-bit Demux Address Bus (3-wires)
+
-
+
-
Signal from Source
SW Trigger/CLK
Signal to Next Shift Reg
IR TOUCH SCREEN INTERFACE: LOW-LEVEL SENSOR BLOCK DIAGRAM

## Slide 2
Tx Emitter Array
Rx Sensor Array
Tx Bank Selector
Tx LED Selector
Rx Bank Selector
Anode To ADC (8 ports)
Anode
Cathode
Cathode
GND
+3.3VDC
Teensy 3.2
Microcontroller
12 port 16bit ADC
3.3V Out
3.3-5V IN
Raspberry Pi
Display
HDMI
USB HID
3-bit addressing
CLK
Horiz/Vert Init Signal
Horiz/Vert Ret Signal
AC Power
IR TOUCH SCREEN INTERFACE: HIGH-LEVEL BLOCK DIAGRAM

## Slide 3
Tx Emitter Array
Rx Sensor Array
Tx Bank Selector
Tx LED Selector
Rx Bank Selector
Anode To ADC (8 ports)
Anode
Cathode
Cathode
Teensy 3.2
Microcontroller
Display Interface
USB HID
3-bit addressing
Horiz/Vert Init Signal
Horiz/Vert Ret Signal

## Slide 4
Select First Horiz Sensor Bank (SW Trigger/Clock Pulse increments Shift Register)
Select Tx Sensor (n)
(Universal Demux Address Bus)
Read Rx ADC (n)
Low Number (Light)
High Number (Blocked)
Store Value in SW Array
Repeat Sensor Select and ADC Read for n Sensors
Select Next Sensor Bank (SW Trigger increments Shift Register)
SW Interrupt Triggers End of Sensors for Horiz
Repeat Process for Vertical
SW Interrupt Triggers End of Sensors for Vertical
Parse Horiz/Vertical Value Arrays for High ADC Readings
Use Index of High Reading to Determine Position
Apply Mean Smoothing Algorithm
Send Mouse Commands to Computer
Repeat Process
IR TOUCH SCREEN INTERFACE: BASIC FLOW CHART